## Slide 2
IoT Device
Gateway
TCP/IP
Socket Server Application
Raw Data Validate , Process and insert
Cloud Storage
Server Program
Web UI
REST API Request
Device Layer
Transport Layer
Aggregation Layer
Processing Layer
Application Layer

## Slide 3
Cloud Storage
IoT Service
IoT Devices and Gateways
Web APP
Mail Send
Join Company UI
Company UI
Application Layer Overview

## Slide 4
Gateway
Raw Data Packet
Device Layer overview
IoT Service
Cloud Storage
Raw Data Packet Receive
Raw Data Packet Sending
IoT Device
BLE
Mail Send
Web UI
TCP Access

## Slide 5
Standard Version
Gateway | 1
Max Device with One Gateway | 15
Raw data packet size | 13 byte
Temperature Stream interval (std) | 15 min
Humidity Stream interval (std) | 15 min
Device / Day (Temperature Stream Data 15 minute interval) | 96 records
Device/ Day (Humidity Stream Data 15 minute interval) | 96 records
Temperature Data Gateway/Day(15 device) | 1440 records
Humidity Data Gateway/Day(15 device) | 1440 records
Gateway Alive Ping alert every minute | 1440 {Updating last alive time in gateway table)
Total Packet sending from Gateway /Day | 4320 Packets(56160 byte)
Advanced version
Gateway | 1
Max Device with One Gateway | 15
Raw data packet size | 13 byte
Temperature Stream interval (adv) | 5 min
Humidity Stream interval (adv) | 5 min
Device / Day (Temperature Stream Data 5 minute interval) | 288 records
Device/ Day (Humidity Stream Data 5 minute interval) | 288 records
Temperature Data Gateway/Day(15 device) | 4320 records
Humidity Data Gateway/Day(15 device) | 4320 records
Gateway Alive Ping alert every minute | 1440 {Updating last alive time in gateway table)
Total Packet sending from Gateway/Day | 10080 Packets(131,040 byte)
Packet Data information

## Slide 6
Customer/7Eleven
Sanki Service
Alert/Refrigerator not working
Selected sensor
Service Request
Solve the Issue
Update The Status
Issue Solved
Ask Status
1 day
Claim Customer
Customer Service
Service Engineer
Working
Quick Service Closed
Refrigerator Start Working
Service Request
Status of Request
Status of Request Status Update
Process Modeling in Application Layer

## Slide 7
Device and Gateway Firmware Setup
Device
BLE Mobile APP
BLE
install Firmware to selected Device
Gateway
Third-party Desktop APP
TCP
install Firmware to selected Gateway
Gateway
Third-party Desktop APP
TCP
Gateway Config To Server Setup
Module Work mode: TCP Client and Registering
Remote IP: Server IP & Remote Port :Server PORT To Gateway
Device Layer Setup Details