## Slide 1: Lock implementation for CarryPark system
2020/2/26
IT-Bonito
Akira Yoshimoto
Rev. 2.0 2020/3/6
Rev. 3.0 2020/4/6
Rev 3.1 2020/4/8

## Slide 2: Definition of system components (assumed)
Lock The lock device used for keeping the baggage of a customer.
APK The application running on a Smartphone to allow a customer to open/close a lock, and lead customers to payment site when finished
Service server CarryPark server which manages customers and the status of locks.
Holds random number tables to be used for secure communication between a lock and APK. It also generates QR code for each lock.
Pre-registration office The office (or factory) where the lock registration process takes place ,uploading the registration information generated by FW build environment ,then QR code labels for locks generated by the service server are printed out.
Billing/settlement server The server (provided by “TakeMe”?) which is accessed from the APK to complete the payment process. Takes care of various payment method to forward money from customer account to CarryPark account
FW build environment Build the firmware running on a lock device to lock/unlock it via BLE, having secure communication with the service server. At the time of the registration , it also generates deviceID and random number tables.

## Slide 3: System architecture (assumed)
Lock
APK
Service Server (CarryPark)
Billing/
Settlement
Server (TakeMe)
Customer Account
CarryPark account
Various payment method
Internet
Pre-registration/
Daily Operation
Office
BLE
connection
Production Process
Billing
Takeme API
Open/Close
Error report
Battery level
Call back
Statistic

## Slide 4: Assumed process of the delivery of locks
A pair of the random number table ID and random number table (registration info) is generated together with the FW for each device at FW build environment. (the ID is same as the latter 8 digits of deviceID. i.e. CP001-0000000N has random number table 0000000N)
All sets of FW and registration info are forwarded to the pre-registration office. (or put into the cloud like bitbucket .. TBD)
The registration info is uploaded to the service server (or it picks up all data from the cloud like bitbucket where the registration info is saved.. TBD) and the server creates the DB for lock devices and random number tables.
QR code for each lock is generated by the service server and merged into the FW folder at the pre-registration office or in the cloud, depending on which area is used for holding the FW, either pre-registration office or cloud…TBD.
The sets of QR code and the FW build are sent to the factory in the format of SD card or internet folder..TBD
The factory picks up the FW and the QR code for each lock. Burn the ROM with the FW ,print the QR code to the label and attach it to the device.
The factory transports them to the warehouse.

## Slide 5
Register lock
Generate
FW (including random number table)
factory
Service server
Pre-registration
Operation desk
Random number tables
DeviceID
Status monitoring
warehouse
Transport
FW +
QR code
FW build environment
(office or Lab)
FW
Production Process

## Slide 6
Production Process
CP001-00000001 folder 1. Registration info
2. FW binary*1
N folders respectively for CP001-00000001 ~ 0000000N
*１ please see the next page for the ecample
Build Firmware
On PC-A (FW team)
Transfer folders
CP001-00000001 folder
1. Registration_information (UTF8 text file )
Random NumberTableID
RandomNumberTable
DeviceID
Transfer registration info
Send back QR codes
CP001-00000001 folder 1. Registration info
2. FW binary
3. QR code
Merage QR code to each CP001 folder and created a portable storage (SD card ot USB memory) which has all of N folders in it
CP001-00000001 1. Registration info
2. QR code
3. The others….
Generate QR and create DB.
The other data such as location to be added later
Factory
PC-B for
Production
(Carrypark office)

## Slide 7: Example of the output from FW build environment
Examples for folders created by FW build environment
The folder 00000600 is for deviceID CP001-0000600 ,and 00000601 is for deviceID 00000601. Each folder consists of config.json and carrypark-cp001.production.hex.
Config.json is the registration info which has the following data in UTF8. { "deviceId":"CP001-00000600", "randomNumberTableId":"00000600", "randomNumberTable":"aifuaghoh0ahneecaht4EijieXaibairohngeehaechip5aiJeuB5weoNgei7eene2kae7yuyoongeid9Biraid5ahchai6chaikieduBeith2oatiapaem8fa3AJe3eiquaith3geethiexoo1chee1up0poh8quaephaichae7ao2ahxahb2Ogohdooc4oovaiyel5rie0ahPohyiew0nurenaquoal9oiD0tiCheevao0thae5oochaipee9T” }
carrypark-cp001.production.hex is the binary file to be burnt into the lock device

## Slide 8: Security requirement for Open/Close sequence
Close (CHECKIN) must be allowed only for registered users
  The lock checks whether the application is connected to the right server or not . Because there is the possibility that the application has been copied from the other smartphone illegally
  MD5 hash algorithm with random numbers combination ,using a random number table shared with locks and the server is used. (Due to the limitation of the memory of PIC on a lock, SHA-1/2 cannot be used)
Open(CHECKOUT) must be done only by the user who has checked in
  The lock checks ”key” used at CHECKIN timing when CHECKOUT is requested.
Charging start/stop must be done correctly
  The lock checks whether the application is connected to the server or not.

## Slide 9: Assumed customer operation (Check In)
DL the APK beforehand
Register her/himself to the Service from the APK with her/his favorite payment method
Visit the location where the lock is installed.
Activate the APK again, login to the service and scan the QR code on the lock
Confirm that the lock device is ready for use
Perform payment for the initial payment
Select “lock”
Put her/his baggage to the lock and latch it manually
Confirm the “locked” message
Leave the venue

## Slide 10: CHECK IN sequence
Any error Smartphone encountered to be reported to the server. Once any error is detected, Smartphone must disconnect the BLE connection. CP001 will forget everything.

## Slide 11: CHECK IN sequence
Any error Smartphone encountered to be reported to the server. Once any error is detected, Smartphone must disconnect the BLE connection. CP001 will forget everything.

## Slide 12: CHECK IN sequence
Any error Smartphone encountered to be reported to the server. Once any error is detected, Smartphone must disconnect the BLE connection. CP001 will forget everything.

## Slide 13: Assumed customer operation (Check out)
Return to the location where the baggage have been kept.
Activate the APK again, login to the service and scan the QR code
Confirm the connection with lock (APK should show the lock number and get it connected as indicated)
Complete payment process on “TakeMe” site.
Select “unlock”
Take her/his baggage out from the lock device manually
Leave the venue

## Slide 14: CHECK OUT sequence
Any error Smartphone encountered to be reported to the server. Once any error is detected, Smartphone must disconnect the BLE connection. CP001 will forget everything, but Hash value

## Slide 15: CHECK OUT sequence
Any error Smartphone encountered to be reported to the server. Once any error is detected, Smartphone must disconnect the BLE connection. CP001 will forget everything, but Hash value

## Slide 16: How to use random number table and MD5 hash calculation
Example of random number table*1 { ”deviceId":”CP001-00000100", "randomNumberTableId":"00000100", "randomNumberTable":"Phanapei0zej4ahYoo3yee6UMiu9zo1iqu5aiReughiuT5peePuShaiCuaTho4qua0PuoluW1EeJahzi6Ujei9OgoSee3ieno0johvu9ToPhah9Ahquoh2za4oaw6Oorohqu1eisei8ceithongie4soh3wie3oR8Yab6IaYoarohwuv5jaij0XooNgieMiethiebeijae2quie8aeBiew5ohbohPahshohvaitheeYeefa2ahyaet2ais8yei4p” }
Remarks: *1. The above table is just an example. The actual tables are generated by FW build environment for a device by device basis together with its deviceID as described before, having characters from “0~9”, “A~Z” and “a~z”.

## Slide 17: How to use random number table and MD5 hash calculation
How to pick up random numbers
  Example of parameters informed from the FW of the lock. X = Starting position = 5 Y = Length of the key = 16 Z = distance to the next = 7
  How the string is made. 1st character = a (the 5th digit from the beginning of the table) 2nd character = j (the 12th (= 5 + 7) from the beginning of the table) 3rd character = 3 (the 19th (=12 + 7) from the beginning of the table) 4th character = i (the 26th) … 15th character = u (the 103rd) 16th character = h (the 110th) Phanapei0zej4ahYoo3yee6UMiu9zo1iqu5aiReughiuT5peePuShaiCuaTho4qua0PuoluW1EeJahzi6Ujei9OgoSee3ieno0johvu9ToPhah9Ahquoh2za4oaw6Oorohqu1eisei8ceithongie4soh3wie3oR8Yab6IaYoarohwuv5jaij0XooNgieMiethiebeijae2quie8aeBiew5ohbohPahshohvaitheeYeefa2ahyaet2ais8yei4p
  Finally, 16 (= Length) characters string is made. “aj3iqupaoueUonuh”

## Slide 18: How to use random number table and MD5 hash calculation
The usage of MD5 In the proposed sequence, hash is calculated for the string (“close”or“open” + “MSG1” + “key picked up from the random number table”).
  “close” = ASCII character string “close” is used for CHECKIN sequence
  “open” = ASCII character string “open” is used for CHECKOUT sequence
  “MSG1” = ASCII character string “1A2B”in the example (but it should be also random string generated in the smartphone and must be 4 characters from ”0~9”, “a~z” and “A~Z”. [0-9a-zA-Z]{4} ) This value is used to create parameters “x”, “y” and “z”. In order to create different set of X,Y and Z every time, MSG1 must consist of randomly generated characters.
  “key” = “aj3iqupaoueUonuh” as composed in the previous page.
That is, MD5 algorithm is applied for the string (respectively for close case and open case) “MSG2” = “close1A2Baj3iqupaoueUonuh” or “open1A2Baj3iqupaoueUonuh”
  As both of the server and the FW shares the same random number table (the ID is the same as the last 8 digits of the deviceID), the hash value at the both ends must be the same.
  The result of digest (128bits) must be converted to 32 ASCII characters string of “0~9” and “a~z”. [0-9a-z]{32}
    E.g. 0x0c94fc99339f ….  0x30633934666339….. = “0”“c””9””4””f””c””9”………
FW will check the hash value to make sure that it is connected to the correct server through the smartphone. Even if someone copied the application and put it into his phone, it cannot provide the correct Hash value without talking to the server, though he would be able to connect his phone to the lock via BLE.

## Slide 19: Commands and responses applied from CP-001 FW Ver 0.30

## Slide 20
cl; and op; to be removed in ver.0.40 and later as they are not safe for commercial products

## Slide 23: Thank you